## Slide 1: HoMonit: Monitoring Smart Home Apps from Encrypted Traffic
Wei Zhang1, Yan Meng1, Yugeng Liu1, Xiaokuan Zhang2, Yinqian Zhang2, and Haojin Zhu1
1Shanghai Jiao Tong University
2The Ohio State University
October, 2018

## Slide 2: Outline
Background
Motivation
Design Overview
DFA Building via SmartApp Analysis
Misbehavior Detection via Wireless Fingerprint
Evaluation
Discussion
Conclusion

## Slide 3: Background
Smart home, a concept of Internet of Things (IoT)
Internet of Things
Smart Home
Client
Cloud
Control multiple devices and let them work together

## Slide 4: Background
Rapid growth of smart home market
Household Penetration
32.0% in 2018
Expected to hit 53.1% by 2022
Market Revenue
$18,877 million in 2018
  Annual growth rate: 14.8%
＊Source: Statista, 2018

## Slide 5: Smart Home Platforms
Smart devices are produced by different vendors
Smart Home Platform:
inter-vendor compatibility
software development ecosystems
Enable different devices to communicate through a local gateway or cloud backend
Control multiple devices and let them work together

## Slide 6: Smart Home Platforms
Prominent examples of smart home platforms
Google Home
Apple HomeKit
Amazon Echo
A popular platform promoted by Samsung
A developer-friendly ecosystem
Support 133 device types and 181 SmartApps in the official GitHub repo
Platform to study in our work

## Slide 7: SmartThings
SmartThings architecture

## Slide 8: SmartThings
SmartThings architecture
SmartThings Cloud Backend
Brain of smart home
Remotely control smart devices
Communicate with user
Host device handlers and SmartApps

## Slide 9: SmartThings
Cloud: Device Handler
Virtual representations of physical devices
Abstract away the implementation details of the protocols for communicating to the devices
Specify the capabilities of these devices
Light
Capability
switch
Commands
on()
off()
SmartThings architecture

## Slide 10: SmartThings
SmartThings architecture
Cloud: SmartApps
Groovy-based programs
Automate devices with capabilities
181 SmartApps (open source) in the official GitHub repository
52 SmartApps (closed source) in SmartThings Marketplace

## Slide 11: SmartThings
SmartThings architecture

## Slide 12: SmartThings
SmartThings architecture
Local Smart Home
Smart Devices
Key building blocks of the entire infrastructure
Connect to the hub with communication protocols
SmartThings Hub
Mediate the communication with all connected devices
Serve as the gateway to the SmartThings cloud
Device 1
Device 2
Device 3
Device 4
Hub
cloud

## Slide 13: SmartThings
SmartThings architecture
Communication Protocols for Smart Home
Wireless standards designed for IoT
Low data transmission rate
Low power consumption
Support AES Encryption

## Slide 14: SmartThings
SmartThings architecture
User interface

## Slide 15: Smart Home Security
Misbehaving SmartApps
Platform (SmartThings) - Attack
Security analysis of emerging smart home applications
Fernandes et al. (S&P 2016)
            Identify several design vulnerabilities of SmartThings
  Over-privileged accesses
  Event spoofing

## Slide 16: Threat Model
Over-privileged access : gaining control of the smart device capabilities which are not granted by the user

## Slide 17: Threat Model
Event spoofing : spoofing event on cloud backend to trigger actions

## Slide 18: Smart Home Security
Existing works mainly fall in to three categories
Platform (SmartThings) - Defense
Apply information flow control to confine sensitive data
Flowfence (USENIX Security 2016)
Context-based permission system
ContexIoT (NDSS 2017)
Enforce context-aware authorization by app analysis
SmartAuth (USENIX Security 2017)
Platform modification
Patching SmartApp

## Slide 19: Smart Home Security
Existing works mainly fall in to four categories
Platform (SmartThings) - Defense
Apply information flow control to confine sensitive data
Flowfence (USENIX Security 2016)
Context-based permission system
ContexIoT (NDSS 2017)
Enforce context-aware authorization by app analysis
SmartAuth (USENIX Security 2017)
Is it possible to find a detection system without platform modification or app patching?

## Slide 20: Our Design: HoMonit
HoMonit : a novel platform-independent anomaly detection system for monitoring smart home apps
Encrypted traffic
Can we detect SmartApp misbehavior from its encrypted traffic?

## Slide 21: Outline
Background
Motivation
Design Overview
DFA Building via SmartApp Analysis
Misbehavior Detection via Wireless Fingerprint
Evaluation
Discussion
Conclusion

## Slide 22: Motivation
SmartApp
Motion
Hub
Switch
Device

## Slide 23: Motivation
SmartApp
Motion
Hub
Switch
Device

## Slide 24: Motivation
SmartApp
Motion
Hub
Switch
Device

## Slide 25: Motivation
SmartApp
Motion
Hub
Switch
Device
similar

## Slide 26: Motivation
SmartApp
Motion
Hub
Switch
Device
different

## Slide 27: Motivation
SmartApp
Motion
Hub
Switch
Device
Applied protocols are designed for low data rate and low power consumption
Event traffic usually has unique and fixed pattern
Protocols have low entropy property

## Slide 28: Motivation
SmartApp
Another observation
Working logic  state machine
Traffic  state machine

## Slide 29: Motivation
Motion
Hub
Switch
Current working SmartApp
  Over-privileged accesses
  Event spoofing
Misbehaviors
sniffer
infer
Inconsistent working logic
benign
Basic idea of HoMonit

## Slide 30: Challenges
How to automatically extract the control logic (i.e., DFA) of both open-source and closed-source SmartApps?

## Slide 31: Challenges
How to automatically extract the control logic (i.e., DFA) of both open-source and closed-source SmartApps?
How to automatically capture wireless traffic (i.e., ZigBee and Z-Wave) and conduct side-channel inference to detect SmartApp misbehaviors?

## Slide 32: Challenges
How to automatically extract the control logic (i.e., DFA) of both open-source and closed-source SmartApps?
How to automatically capture wireless traffic (i.e., ZigBee and Z-Wave) and conduct side-channel inference to detect SmartApp misbehaviors?
How to implement and evaluate detection accuracy in a real-world smart home deployment?

## Slide 33: Outline
Background
Motivation
Design Overview
DFA Building via SmartApp Analysis
Misbehavior Detection via Wireless Fingerprint
Evaluation
Discussion
Conclusion

## Slide 34: System Workflow

## Slide 35: System Workflow
How to extract the control logic of both SmartApps?
How to capture wireless traffic and conduct side-channel inference?

## Slide 36: Outline
Background
Motivation
Design Overview
DFA Building via Benign SmartApp Analysis
Misbehavior Detection via Wireless Fingerprint
Evaluation
Discussion
Conclusion

## Slide 37: DFA Building via SmartApp Analysis

## Slide 38: DFA Building via SmartApp Analysis
We utilize Deterministic Finite Automaton (DFA) to model SmartApp and build the model by app analysis
transition
start state
symbol
accept state

## Slide 39: DFA Building via SmartApp Analysis
We handle app analysis in two perspectives:
Open-source SmartApps → Static code analysis
Closed-source SmartApps → NLP analysis

## Slide 40: DFA Building for Open-source Apps
Take a SmartApp Smart Light as example
It turns light on when motion is detected
Therefore, it automates two devices
Source code:
Static analysis

## Slide 41: DFA Building for Open-source Apps
We achieve DFA building in two steps:
Source code → AST → DFA
We use AstBuilder to convert code into Abstract Syntax Tree (AST).
The translation from AST to DFA is completed based on SmartApp characteristics

## Slide 42: DFA Building for Open-source Apps
preferences → capability
[motionSensor]
[switch]
subscribe
→ command & attribute
[motion.active]
DFA building: infer DFA symbols

## Slide 43: DFA Building for Open-source Apps
Preferences block statement
Extract the capabilities requested by DFA
Subscribe method
Further determine the specific symbols of DFA
symbol

## Slide 44: DFA Building for Open-source Apps
subscribe
→ initial transition
S0 → [motion.active] → S1
Handler method
→ intermediate transition S1 → [switch.on())] → S2
DFA building: infer DFA transitions

## Slide 45: DFA Building for Open-source Apps
Subscribe method
Indicate one transition from start state to intermediate state
Handler method (may contain if-else logic)
Determine how the state will transition to other states
transition & states

## Slide 46
What if we do not have access to the source code of SmartApps?

## Slide 47: DFA Building for Closed-source Apps
Still the same SmartApp
Smart Light
Now turn our eyes towards its app interface (i.e., UI)
Prompt Sentences
Working logic

## Slide 48: DFA Building for Closed-source Apps
Text extraction
Symbol inference
DFA building
Our method
NLP

## Slide 49: DFA Building for Closed-source Apps
Text extraction
Symbol inference
DFA building
We apply uiautomator to convert the UI hierarchy into XML nodes and then extract the text
<node index="0" text="When water is sensed"
Resource-id="com.smartthings.android:id/title">

## Slide 50: DFA Building for Closed-source Apps
Text extraction
Symbol inference
DFA building

## Slide 51: DFA Building for Closed-source Apps
Symbol inference
UI text
Alarm
Color Control
Color Temperature
Switch
Switch Level
Light
Power Meter
Outlet
Capability candidate sets
NLP Analysis
Switch.on()
Final symbol
Directly applying NLP for UI text can not achieve good performance

## Slide 52: DFA Building for Closed-source Apps
Text extraction
Symbol inference
DFA building
Our strategy : reduce candidate numbers before using NLP
Directly applying NLP for UI text can not achieve good performance
No adequate training data for SmartThings

## Slide 53: DFA Building for Closed-source Apps
Text extraction
Symbol inference
DFA building
Candidate reduction
Text descriptions for SmartApps require a unique language model
However, our training set is inadequate
Our strategy : test all the device candidates for a certain SmartApp and reduce the candidate set in advance
Reduced candidate device set
Test each options

## Slide 54: DFA Building for Closed-source Apps
Text extraction
Symbol inference
DFA building
Candidate reduction
Text descriptions for SmartApps require a unique language model
However, our training set is inadequate
Our strategy : test all the device candidates for a certain SmartApp and reduce the candidate set in advance
Capability candidate set
Alarm
Switch
Switch
Power Meter
Outlet
Color Control
Color Temperature
Switch
Switch Level
Light
Switch
Reduced
capability
candidates
∩
Reduced to 1

## Slide 55: DFA Building for Closed-source Apps
UI text
Alarm
Color Control
Color Temperature
Switch
Switch Level
Light
Power Meter
Outlet
Before
NLP
Switch.on()
Final symbol
Switch
NLP
After
hard
easy

## Slide 56: DFA Building for Closed-source Apps
Text extraction
Symbol inference
DFA building
NLP analysis
NLTK : extract the noun phases and verb phrased for capability analysis
water → Water Sensor
Word2Vec : analyze the context of the verb phrases and then determine the state of attributes or commands
when water is sensed → water.wet

## Slide 57: DFA Building for Closed-source Apps
Text extraction
Symbol inference
DFA building

## Slide 58: DFA Building for Closed-source Apps
Text extraction
Symbol inference
DFA building
DFA building
UI design follows the symbol logical relationship
Chain the symbols according to the UI layout
“ When there is movement, turn on a light ”
Symbol
logic

## Slide 59: Outline
Background
Motivation
Design Overview
DFA Building via SmartApp Analysis
Misbehavior Detection via Wireless Fingerprint
Evaluation
Discussion
Conclusion

## Slide 60: Misbehavior Detection via Wireless Fingerprint
Event Inference
DFA Matching
Traffic collection

## Slide 61: Event Inference
Filtering noise traffic
Fingerprinting events
Inferring events
Traffic collection
ZigBee traffic
TI CC2531 USB Dongle
802.15.4 monitor
2.4GHz
Z-Wave traffic
USRP
Scapy-Radio
908.4MHz and 916MHz
Traffic collection

## Slide 62: Event Inference
Filtering noise traffic
Fingerprinting events
Inferring events
Filtering noise traffic
Beacon packets
Used for acknowledging data transmission and maintaining established connection
Retransmission packets
Used for transmission failure
Unrelated traffic
Traffic from devices using other wireless standards (e.g., WiFi)
Traffic collection

## Slide 63: Event Inference
Filtering noise traffic
Fingerprinting events
Inferring events
Filtering noise traffic
Beacon packets
Used for acknowledging data transmission and maintaining established connection
Retransmission packets
Used for transmission failure
Unrelated traffic
Traffic from devices using other wireless standards (e.g., WiFi)
Traffic collection

## Slide 64: Event Inference
Filtering noise traffic
Fingerprinting events
Inferring events
Fingerprinting events
We adopt Levenshtein Distance to measure the similarity between packet sequence
Traffic collection
fingerprint
event type
collected packet sequence

## Slide 65: Event Inference
Filtering noise traffic
Fingerprinting events
Inferring events
Fingerprinting events
We adopt Levenshtein Distance to measure the sequence similarity between packet sequence
Traffic collection
fingerprint
event type
collected packet sequence
Packet sequence
Event name
Device name
Protocol
switch.off
Samsung SmartThings Outlet
ZigBee
Fingerprint
50 ↓ 47 ↓ 47 ↓ 52 ↓
50 ↓ 47 ↓ 47 ↓ 52 ↓
50 ↓ 47 ↓ 47 ↓ 52 ↓ 52 ↓
50 ↓ 47 ↓ 47 ↓ 52 ↓
50 ↓ 47 ↓ 47 ↓ 52 ↓
50 ↓ 47 ↓ 52 ↓
50 ↓ 47 ↓ 47 ↓ 52 ↓
…
Smallest distance

## Slide 66: Event Inference
Filtering noise traffic
Fingerprinting events
Inferring events
Inferring events
Partition the traffic flow into a set of bursts (a group of consecutive packets within burst threshold)
Match the burst with the possible fingerprint by calculating their Levenshtein Distance
Traffic collection
Fingerprints for event types supported by 11 devices

## Slide 67: Event Inference
Filtering noise traffic
Fingerprinting events
Inferring events
Inferring events
Partition the traffic flow into a set of bursts (a group of consecutive packets within burst threshold)
Match the burst with the possible fingerprint by calculating their Levenshtein Distance
Traffic collection
Find smallest

## Slide 68: SmartApp Misbehavior Detection
Output
Accept state:
Otherwise a misbehaved SmartApp is detected
Process
Input
Initially, . For each event in sequence, transition DFA if
A sequence of events
DFA matching algorithm

## Slide 69: SmartApp Misbehavior Detection
Over-privilege accesses
Event spoofing
Raising extra device event
Skipped states
Benign
Misbehaving

## Slide 70: Outline
Background
Motivation
Design Overview
DFA Building via SmartApp Analysis
Misbehavior Detection via Wireless Fingerprint
Evaluation
Discussion
Conclusion

## Slide 71: Testbed
ZigBee sniffing : TI CC2531 USB Dongle
Z-Wave sniffing : two USRPs
Distance between SmartThings hub and HoMonit is 7 feet
Dataset : 30 open-source SmartApps from
SmartThings Public GitHub Repository
Smart devices : 7 ZigBee devices (20 app) and 4 Z-Wave devices (10 app)

## Slide 72: Misbehavior Detection
Reconsider the two types of attacks…
Platform (SmartThings) – Misbehavior types
  Earlence Fernandes, Jaeyeon Jung, and Atul Prakash. 2016. Security analysis of emerging smart home applications. In IEEE Symposium on Security and Privacy (S&P).
  Over-privileged accesses
    Illegally obtaining accesses to command / all the capabilities of the devices
  Event spoofing
    A malicious SmartApp with the knowledge of the hub and device identifiers can spoof an arbitrary event
  No available misbehaving app dataset:

## Slide 73: Misbehavior Detection
Over-privileged accesses
Over-privileged access realization
We develop over-privileged apps by adding malicious code to cause unintended operations
Strategy
HoMonit detects this misbehavior by checking additional states in DFA matching process
Experiment
30 benign & misbehaving apps
3 volunteers to simulate residents
20 times triggering for each app

## Slide 74: Misbehavior Detection
Event spoofing
Event spoofing realization
We develop event-spoofing apps by exploiting insufficient event protection mechanism to spoof a physical event and trigger subscribed apps
Strategy
HoMonit detects this misbehavior by checking missing states in DFA matching process
Experiment
Same approach as over-privilege access evaluation

## Slide 75: Misbehavior Detection Result
Metrics
TP (true positive) : Correctly labeled misbehaving SmartApp
TN (true negative) : Correctly labeled benign SmartApp
FP (false positive) : Incorrectly labeled benign SmartApp
FN (false negative) : Incorrectly labeled misbehaving SmartApp
TPR (true positive rate) : TPR = TP / (TP + FN)
TNR (true negative rate) : TNR = TN / (FP + TN)

## Slide 76: Misbehavior Detection Result
Metrics
TP (true positive) : Correctly labeled misbehaving SmartApp
TN (true negative) : Correctly labeled benign SmartApp
FP (false positive) : Incorrectly labeled benign SmartApp
FN (false negative) : Incorrectly labeled misbehaving SmartApp
TPR (true positive rate) : TPR = TP / (TP + FN)
TNR (true negative rate) : TNR = TN / (FP + TN)
Detection result of 60 misbehaving SmartApps

## Slide 77: Misbehavior Detection Result
Metrics
TP (true positive) : Correctly labeled misbehaving SmartApp
TN (true negative) : Correctly labeled benign SmartApp
FP (false positive) : Incorrectly labeled benign SmartApp
FN (false negative) : Incorrectly labeled misbehaving SmartApp
TPR (true positive rate) : TPR = TP / (TP + FN)
TNR (true negative rate) : TNR = TN / (FP + TN)
Detection result of misbehavior occurrence in SmartApps
The average TPR for over-privileged accesses is 0.98
The average TPR for event spoofing is 0.99
Failed test case reason : packet loss, unexpected wireless traffic, accidental signal reception delay

## Slide 78: Outline
Background
Motivation
Design Overview
DFA Building via SmartApp Analysis
Misbehavior Detection via Wireless Fingerprint
Evaluation
Discussion
Conclusion

## Slide 79
Thought
Our presented approach can be potentially applied to other IoT systems
Generality
We also investigate IFTTT, an open-source platform compatible with SmartThings
IFTTT
The events present the same wireless fingerprints &
Applets share similar logic
Result

## Slide 80: Privacy Consideration
Daily routines : The attacker can spy on the victim’s daily activities
SmartApp Example
Good Night : change its mode when there is no human activity in the home
Side-channel information leakage is a double-edged sword
Health conditions : The attacker can infer the health condition of residents
SmartApp Example
Elder Care: Slip & Fall : monitor the behavior of the aged people
Home occupations : The attacker can infer it by detecting the app existence
SmartApp Example
Vacation Lighting Director : deceptively control lights while residents are away
However, this side-channel inference attack requires placing a wireless sniffer in the proximity of smart home

## Slide 81: Outline
Background
Motivation
Design Overview
DFA Building via SmartApp Analysis
Misbehavior Detection via Wireless Fingerprint
Evaluation
Discussion
Conclusion

## Slide 82: Conclusion
Performance
HoMonit can effectively validate the working logic of SmartApps and achieve a high accuracy in the detection of SmartApp misbehaviors
Contribution
Program logic extraction from source code or UI, and auto DFA construction & matching algorithms
Insight
Leverage the side-channel information leakage in the wireless channel to infer device event
HoMonit
An anomaly detection system for smart home platforms to detect misbehaving SmartApps

## Slide 83
Q & A
Upcoming release: nsec.sjtu.edu.cn
Thanks!